## Slide 1: Sacramento Ductless Heat Pump Demonstration
Tom Eckhart/Greg Sullivan, UCONS
February, 2016

## Slide 2: Presentation Overview
Objective:
Provide update to Sacramento DHP demonstration.
Also:
Seeking TF feedback on status and next steps
Utility direction on future technology demonstrations
Questions for TF

## Slide 3: Summary of Sacramento Research Plan
Objective:
Evaluate the energy performance, temperature distribution, and occupant comfort of high efficiency, single-head, ductless heat pumps (DHP) installed in four Sacramento area manufactured homes.
Rationale:
  Small study to initiate data collection, understand occupant behavior/satisfaction.
  Data useful to confirm potential future activities, e.g., modeling, calibration, program development
  Outcomes to assist in informing larger study

## Slide 4: Summary of Sacramento Research Plan
Research Questions:
1. What fraction of the total cooling load will a single-head DHP be able to satisfy over the cooling season?
2. Of the fraction of cooling load displaced, what are the resulting energy savings in comparison to the existing central air conditioning system?
3. What are the differences in zonal temperature distributions (DHP versus existing AC) across the major living zones (living room, kitchen/dining, and bedrooms)?
4. In comparison to the central AC, how well does the DHP provide for occupant comfort? This research question will be answered through occupant surveys.

## Slide 5: Summary of Sacramento Research Plan

## Slide 6: Summary of Sacramento Research Plan

## Slide 7: Preliminary Results
Existing System Daily Energy and Temperature Profile

## Slide 8: Preliminary Results
Ductless Heat Pump Daily Energy and Temperature Profile

## Slide 9: Preliminary Results
Daily Combined HVAC Energy and Temperature Profile

## Slide 10: Preliminary Results
Daily Combined HVAC Energy and Temperature Profile

## Slide 11: Preliminary Results
Home A
Pre/post savings analysis - comparable weather days:
Average Existing AC pre-kWh/day: 19.5
Average HVAC DHP kWh/day: 13.6
Average HVAC savings kWh/day: 5.9
Average HVAC savings %: 30.3 %
Runtime Tally
Percent Runtime Existing AC 18.5 %

## Slide 12: Preliminary Results
Average HVAC Energy Savings Percentage – Post DHP Installation
Chart: 
| Home D | Home A | Home C | Home B
Percent Savings | 0.24638 | 0.30256 | 0.47651 | 0.6369

## Slide 13: Preliminary Results
Average Existing HVAC System Runtime Percentage – Post DHP Installation
Chart: 
| Home B | Home C | Home A | Home D
Percent Runtime | 0 | 0.0168 | 0.1845 | 0.2867

## Slide 14: Preliminary Results: Research Questions
Research Questions:
1. What fraction of the total cooling load will a single-head DHP be able to satisfy over the cooling season?
      Homes studied to date report 70 % – 100%
2. Of the fraction of cooling load displaced, what are the resulting energy savings in comparison to the existing central air conditioning system?
      Homes studied to date report 25% – 64%
3. What are the differences in zonal temperature distributions (DHP versus existing AC) across the major living zones (living room, kitchen/dining, and bedrooms)?
      Living room comparable profile, back bedrooms warmer (2 F to 10 F)
4. In comparison to the central AC, how well does the DHP provide for occupant comfort? This research question will be answered through occupant surveys.
      DHP well received, survey forthcoming

## Slide 15: Next Steps/Questions
Seeking TF feedback on status and next steps
Utility direction on future technology demonstrations
Questions for TF
  Path for follow-on larger study
    Validate savings
    Customer behavior/comfort/acceptance
    Funding options and process for approval?
  Thank you.

## Slide 16: Additional Slides
  Additional Home Data
  Preliminary CVRH Cooling Season Findings
  Relevant DHP Incentives in Pacific Power (N. California) Territory

## Slide 17: Preliminary Results
Existing System Daily Energy and Temperature Profile

## Slide 18: Preliminary Results
Existing System Daily Energy and Temperature Profile

## Slide 19: CVRH Cooling Season Preliminary Findings
  Findings not made public – for discussion purposes only

## Slide 20: Pacific Power (N. California) DHP Incentive Program
Ductless Heat Pumps
Get up to $1,500 cash back
Go ductless and find your comfort zone
Make the move to a ductless heat pump and earn up to $1,500 cash back on your purchase.
Enjoy savings of up to 50 percent on your heating and cooling costs, and with no invasive ductwork, installation is easy and affordable.
  http://www.homeenergysavings.net/homeowner/category/heating-and-cooling/in/california/ductless-heat-pumps?region=california